## Slide 1: Weekly Report
Report on last week
  It was possible to apply RL to event-triggered control
  It will be applicable to self-triggered control as well
  (At least with same steps,) it was not conducted well
    Algorithm did not converge
  Conjecture:
    The control performance changes rapidly with little parameter change
  If the conjecture is valid, research the condition and consider solution
Check the validity (conclusion: NO)

## Slide 2: Weekly Report
Recently experienced data
This scatter plot does not show control path
Although parameter changes slightly, control path changes drastically(?)
(rad)
(rad/s)

## Slide 3: Weekly Report
Depict control path for each episode(new starting point)
It is not possible to see why policy became bad with this picture
  (P1) Control path suddenly changed in second episode (conjecture)
  (P2) Overfit to blue path
  (P3) Other reason
Assume
  Policy parameters are updated in all steps
  Initial policy stabilize all initial states

## Slide 4: Weekly Report
How the policy changes in 2nd episode
  Pick up policy in equally step interval
    ex.) step 100, 200, 300, ...
  (Attention: policy are not updated in each path)
Control path does not change suddenly
  The conjecture is not valid
detail

## Slide 5: Weekly Report
Next step: Reconsider the cause for policy deterioration
  policy gradient approximation
    This assumes experienced states is well approximates
    In other words, improve policy by prioritizing only experienced states
    Lack of the number of episodes makes policy overfitting
  For data efficiency, by enlarging minimum interval time, increase the number of control paths in replay buffer (N steps experienced data)

## Slide 6: Weekly Report
By changing learning configuration as last slide, policy may improved
  Distribution of replay buffer
  Learned policy
There is no divergent paths
There is no guarantee that this policy is the best policy …
Wide interval around origin and frequent otherwise
Stabilize the system

## Slide 7: Weekly Report
This week
  Reconsider and discuss the theme
  Ideas for stable learning
    Configuration of optimizer (learning late hyperparameter etc..)
    Safe learning